## Slide 1: SURF 2024 – 7th Meeting
Ryan Hsieh 2024/07/05

## Slide 2: AGENDA
Optimization Model - Power Flow Studies relationship with BreakThrough Energy
BreakThrough Grid Data vs EPA Data

## Slide 3: Power flow studies
Optimal Power Flow (Load Flow) analysis : determine the optimal operating conditions for power system
Aiming...:
  Minimizing : generation cost, power loss, or environmental impact
  Satisfying : set of constraints
    Power balance, voltage limit, or generation limit
  Outputs : Optimal generation dispatch, bus voltages, and power flow on transmission lines
Reduced Power Flow analysis : Simplified power flow analysis method = reduces complexity of full power flow problem
Aiming...:
  Making : Approximation or assumptions to streamline the computation
  Quick analysis & decision making when the full power flow study is too time consuming
  Outputs : Not accurate enough comparing to OPF = only use as insights

## Slide 4: Breakthrough Energy Packages
REISE.jl
Julia-based tool for renewable energy integration simulation
2. PowerSimData
Python-based tool creating & managing simulation scenarios for power system analysis
3. PostREISE
Post processing tool that works with REISE.jl & PowerSimData
Large scale power systems & optimizing the integration of renewable sources
Bridge between data management, scenario creationg, and simluation execution
Provides function for analysis, visualizations, interpreting results of simulations
DC-OPF
Simplifies AC Power Flow equations by making linear approximations ==> reduce computational complexity while providing accurate results for high-level planning & optimization study
Leveraging efficiency & scalability of handling large datasets and complex scenarios

## Slide 5: Proof to be DC-opF
Three Major Assumptions:
  Voltage Magnitude: Voltage magnitudes are assumed to be constant and close to 1.0 per unit.
  Voltage Angles: Voltage angle differences between buses are assumed to be small.
  Reactive Power: Reactive power and losses are ignored.

## Slide 6: Breakthrough Grid Data vs EPA Data
Generation of Energy data

## Slide 7: Miso regions vs. EPA regions
Focus on MISO region including states:
Completed States:
  Arkansas ---> 75 counties
  Illinois ---> 102 counties
  Indiana ---> 92 counties
  Iowa ---> 99 counties
  Louisiana ---> 64 counties
  Michigan ---> 83 counties
  Minnesota ---> 87 counties
  Mississippi ---> 82 counties
  Montana ---> 56 counties
  Wisconsin ---> 72 counties
Partial States:
  Kentucky ---> 4 counties only
  Missouri ---> 15 counties only
  N. Dakota ---> 5 counties only
  S. Dakota ---> 6 counties only
  Texas ---> 14 counties only

## Slide 8: Gen Data Comparison
Generation Data from EPA
Generation Data from BE
More detailed w/ percentage cover
MWh
- Gwh

## Slide 9: PostREise
PostReise generated plot
These are the sample bar plots for generation vs capacity of all types of energy in CA and Western Region